## Slide 1: Loki USB Hardware Diagram
Laptop Computer
USB Hub
Laser Ranger
Kinect
Left Camera
Right Camera
Bluetooth
Arduino
Shoulder
Servos
Wheels
Microsoft Kinect. Tilt Controlled byAX12 Servo
Logitech QuickCam Pro
Logitech QuickCam Pro
Bluetooth for commands from Android Phone
Kerr Motor Controller, controls a Pittman motor for each shoulder
USB2Dynamixel controls Dynamixel MX servos
Pololu Trex Motor controller, drives Pittman wheel motors
Hokuyo URG-04LX-UG01 Laser Rangefinder (optional)
Arduino Mega – handles sensor input, Led lights, etc.

## Slide 2: Sensors & Control
Top
Mid Upper
Mid
Mid Lower
Bottom
Laptop Computer
Arduino
PCF 8574
LED “Eyes”
PCF 8574
GP2Y0D340K IR Bumper
Left Arm
Right Arm
PCF 8574
GP2Y0D340K IR Bumper
I2C-IT IR Sensors
I2C-IT IR Sensors
Head
Arduino Interface Shield
Hamamatsu P5587 Wheel Motor Monitor
Hamamatsu P5587 Wheel Motor Monitor
Left and Right Wheel Monitors
Bumper Switches
Sharp IR Ranges (4)
Front and Side IR Rangers
I2C Compass
Body Lights
I2C

## Slide 3
Robot Control Engine
Control Modules
User Interface
Control Thread Queue
Read Thread
GUI Thread
Remote Control over IP
Socket Read Thread
Socket
Write Thread
Sensor Fusion
User Command
Collision
Behaviors
Object Avoidance
Navigation
Priority
Config and
Manual Control
Arduino
Depth Capture
+ Speech Reco
Vision Processing
Face Recognition Object Detection etc.
Laser Range
Read Laser Add XY, Object Avoidance and Navigation
Laser Thread
Kinect C# App
Write Thread
Sensor
Sensor Data
Camera App Communication
Camera App
Camera Threads
Motor Thread
Smart Servo Thread
Kerr Thread
Control
Kerr Control
Pololu Trex
Dyna 2 USB
Drive Control Arbitrator
Servo Control Arbitrators
Android Phone
Bluetooth
Blue- Smirf
Kinect App Communication
Kinect Threads
Depth Processing
Read Kinect Data Convert Range to XYZ Point Cloud
Depth Thread
General Timers Poll Sensors Keep Alive Ping
Watchdog timeouts
Timer Thread